Intimate Theatre Dimensions, Sound and Lighting Information

Updated: 06/2015

The Intimate Theatre:

Lighting System

ETC Expression 3 Lighting Console, DMX & ETC Protocol

96 – 2.4K Sensor Dimmers

12 Dimmers are paralleled in wall pockets (#1-3 on the Northwest corner, #4-6 on the Northeast corner, #91-93 on the Southwest corner, #94-96 on the Southeast corner).

The dimmers run across the grid from the East wall to the West  wall in (6) lines of 16 dimmers each

Dimmers #1-16 start closest to the North wall and the lines progress south at approximately eight foot intervals, ending with dimmers #81-96 closest to the South wall.

Instruments:

40 Source 4 Leko Bodies

18 with Twist Lock caps

22 with SPG (3-Pin) caps

Barrels:

7-19 degree barrels

10--26 degree barrels

10-36 degree barrels

20-50 degree barrels

29-Source 4 ParNELs

(8 used for audience lighting)

18 with Twist Lock Caps

12 with SPG Caps

3 strip lights – 3 circuits, 4 lamps per circuit.

There are (4) 12’x1 ½” pipe and (4) 50 lb. bases available.

Cables and Connectors:

19 2-fers

1 Male SPG (3-Pin) to Female PBG (Edison)

32 Male SPG to Female Twist Lock

5 Male Twist Lock to Female SPG

1 Male Twist Lock to Female PBG

(28) 5’ Cable

(30) 10’ Cable

(18) 25’ Cable

(10) 50’ Cable

(1) 1,250’ 12/3 SOW-A Cable

(1) 100’ White flexible 12-Gauge wire

(1) 25’ CamLoc standard cable with (1) Ground (green) & (1) Neutral (white) Turnarounds

(1) Response Opto-Splitter

(2) Camlok turnarounds

Edison Cable available

Auxiliary Power:

400amp 3 phase 120/208v w/company switch, posi-loc and bare tails

The Grid:

56'x51' with cross pipes at 8' centers and is approx. 17' (16’11” from bottom of bottom pipes, 17’2” from bottom the top pipes) from the stage floor.  It is also possible for us to add pipes as needed.

10 Swivel 1 ½” Aluminum Cheeseboros are available for piping.

Total Room Size:

60'x60' overall w/ part sprung floor and part poured concrete

The 'sprung' part of the floor:

Centered between the North and South walls

Is 20'x40' running East and West lengthwise, starting 3' from the West wall.

The remainder of the floor is poured concrete.

##### Auditorium Seating

Modular - maximum 250

*Proscenium set-up on north wall facing south is standard – additional charges for change-over to any other configuration

##### Dressing Rooms  (w/ self-contained bathrooms and showers)

#### 2 Rooms (7 Stations each)

Large Loading Door

12’x12’ elephant doors

Audio Equipment

House Console – Midas Verona (32 mono channels/8 stereo channels)

(8) JBL AM6212 Speakers (movable, but a slow move) w/4 amp channels

(4) JBL 18” Subs (permanent)

Amps: 4 channels for the full range mains and 2 channels for the subs

(2) JBL 12” Two-way grid-mounted Monitors

Denon DN-4000 Dual CD Players

Yamaha SPX 990 Processor

(2) DBX 1066 Compressor/Limiter/Gate (4 ch. total)

(1) DBX 166 Compressor/Limiter/Gate

(2) Ashly Protea Graphic Equalizers (4 channels per)

Sony WD820 Wireless System (8 ch.) – 8 Sony HH, 6 Sony Lavs

Communication:

Clear-Com system

(6) Belt packs available

Speaker and microphone hard-mounted in each dressing room